## Slide 1: Road Network Evaluation Tools: Overview, Main Concepts, Applications
Cesar Queiroz, Ph.D.
Consultant, former World Bank Highways Adviser
Arusha, Tanzania, 16-20 September 2013

## Slide 2: RONET Overview, Main Concepts, Background and Applications
Infrastructure and economic development
Optimization defined
A common concern: how to optimize maintenance and rehabilitation
What is required for an agency to use RONET?
RONET structure
RONET applications
Next steps

## Slide 3: Infrastructure
“The built environment in which we live” (Ausubel and Herman)
The physical framework upon which the economy operates and our standard of living depends (ASCE)

## Slide 4: Infrastructure comprises
Public utilities: power, telecommunications, piped water supply, sanitation and sewerage, solid waste collection and disposal, piped gas
Public works: roads, dams, canals, railways, ports, waterways, airports, buildings

## Slide 5: Developing and Developed Countries
Developing countries include low- and middle-income economies
Developed (advanced, industrial, rich) countries denote high-income economies
The World Bank’s main criterion for classifying economies is gross national income (GNI) per capita, previously referred to as gross national product (GNP)
http://data.worldbank.org/indicator/NY.GNP.PCAP.CD

## Slide 6: Classification of Economies
Economies GNI per capita
Low-income $1,035 or less
Middle-Income $1,036 to $12,615
Lower $1,036 to $4,085
Upper $4,086 to $12,615
High-income $12,616 or more
Source: http://data.worldbank.org/about/country-classifications

## Slide 7
Examples of Gross National Income
GNI,
$/cap
Chart: 
| Nor | Swi | US | UK | Slo | Por | Est | Rus | Bra | Bot | Chi | Ser | Bol | Ind | Taj | Tan | DRC
Series 1 | 98860 | 82730 | 50120 | 38250 | 22710 | 20580 | 15830 | 12700 | 11630 | 7720 | 5740 | 5280 | 2220 | 1530 | 860 | 570 | 220
Column1

## Slide 8
Examples of Gross National Income
GNI,
$/cap
Chart: 
| Slo | Est | Rus | Bra | Bot | SA | Chi | Ser | Ukr | Bol | Ind | Lao | Sen | Taj | Tan | Moz | DRC
Series 1 | 22710 | 15830 | 12700 | 11630 | 7720 | 7610 | 5740 | 5280 | 3500 | 2220 | 1530 | 1260 | 1040 | 860 | 570 | 510 | 220
Column1

## Slide 9: Economic Development and Infrastructure
GNI ($/pop)
Source: Queiroz and Gautam
GNI = 1.39 PRD
R squared: 0.76
98 countries

## Slide 10
Road Agency
Budget
Total Road Transport Costs
User Costs
Budget, Costs $
Too
Large
Too Poor
Optimal
Too Good
Optimal
Too
Small
Road Condition
Optimal Road Condition

## Slide 11: Road Network Evaluation Tools
RONET, developed by Rodrigo Archondo-Callao for SSATP, helps decision makers to:
  Monitor network condition
  Plan allocation of resources
  Assess consequences of macro policies
  Design Road Asset Management Systems

## Slide 12: Road Network Evaluation Tools
Availability: RONET is available free of charge on the World Bank website at: http://go.worldbank.org/HWVR0FWEF0
http://go.worldbank.org/FF0CT8M770
General use: RONET can be used in any city, country or region, provided that appropriate data are available
Version 2.00 – latest version, published in 2009

## Slide 13: RONET Version 2.00

## Slide 14: What is Required for an Agency to Take Advantage of Tools Such as HDM-4 and RONET?
Updated road inventory and condition data, e.g., length of roads in each category, pavement structure, road roughness
Traffic data, e.g., volumes by vehicle category, weight of heavy vehicles
Road user cost data, e.g., price of new vehicles, fuel consumption and cost
Unit cost of road works, e.g., rehabilitation ($/km), new construction ($/km)

## Slide 15: Road Network Length Matrix
Total 5 X 5 X 5 X 5 = 625 Road Classes

## Slide 16: International Roughness Index (IRI)
Main road condition indicator used by models such as RONET and HDM
A standard scale used throughout the world to quantify the roughness of roads
The IRI summarizes the roughness qualities that impact vehicle response (such as vehicle vibration)
It relates to overall vehicle ride, operating cost, dynamic wheel loads, and overall surface condition

## Slide 17: Development of IRI
The International Road Roughness Experiment, Brasilia, Brazil, 1982
Reference: World Bank Technical Paper No. 45, “The International Road Roughness Experiment: Establishing Correlation and a Calibration Standard for Measurements,” available at: http://go.worldbank.org/0UUNR93490

## Slide 18: International Roughness Index
Notes: One solution is to pass the profile through the IRI filter before the comparison is made. Instead of just getting an index, you get a filtered profile that is weighted to emphasize what counts to the IRI.

## Slide 19: IRI Meaning and Uses
IRI is determined by measuring the profile along the wheel paths of the road, and then filtering the profiles through a quarter-car mathematical model to simulate the suspension deflection of a passenger car
Its uses include assessing road condition and as a construction specification

## Slide 20: IRI Calculation from Road Profiles
“ProVAL” - Profile Viewing and AnaLysis - an engineering software used to view and analyze pavement profiles, including IRI calculations
Sponsored by the US Federal Highway Administration (FHWA)
Available free of charge from: http://www.roadprofile.com/

## Slide 21: IRI Calculation from Road Profiles
“RoadRuf” – a tool for computing IRI, available from the University of Michigan at: http://www.umtri.umich.edu/divisionPage.php?pageID=62
RoadRuf includes an interactive X-Y plotter and a spectrum analyzer
A sample program for calculating IRI is available at: http://www.umtri.umich.edu/content/IRIMain.f

## Slide 22: RONET Paved Road Deterioration Model
RONET uses simplified incremental road deterioration model for paved roads:
  traffic loading (YE4)
  pavement modified structural number and
  subgrade bearing capacity (SNC)
  pavement age (t)
  environmental coefficient (m)
  existing condition (IRIa)

## Slide 23: Road User Costs Model
Expressed as a polynomial function of roughness for each vehicle category
Developed using World Bank RUCKS (Road User Costs Knowledge System) model
URUC - unit road users’ cost ($/vehicle-km)
IRI - pavement longitudinal roughness (m/km)
a0, a1, a2, a3 - model coefficients that depend on input data (e.g., new vehicle, fuel and tire costs)

## Slide 24: Example of IRI and Road Condition
Very good: IRI less than 2.5 m/km
Good: IRI from 2.5 m/km to 3.5 m/km
Fair: IRI from 3.5 m/km to 5.5 m/km
Poor: IRI from 5.5 m/km to 10.5 m/km
Very poor: IRI higher than 10.5 m/km

## Slide 25: Riverside Freeway, SR 91, CA

## Slide 31: Types of Road Network
Five or less network types can be defined by the user based on functional classification, region, terrain type, or environmental type

## Slide 32: Surface Types
RONET uses five surface types. The country specific characteristics of the surface types are user defined

## Slide 33: Traffic categories vary by surface type

## Slide 34: Road Condition Categories
Very Good: requires only routine maintenance (RM)
Good: requires RM plus preventive maintenance or spot regravelling or repairs
Fair: requires RM plus periodic maintenance
Poor: requires RM plus strengthening or partial reconstruction
Very Poor: requires RM plus full reconstruction

## Slide 35: RONET Main Input Data
Length of road sections (per category, traffic, condition) comprising the network
Unit cost of road works
Selected country data (e.g., discount rate, fuel cost, salaries, vehicle fleet, traffic growth rate)

## Slide 36: Current Asset Value Calculation

## Slide 37: Performance Assessment
What are the consequences of different budget scenarios?

## Slide 38: RONET evaluates alternative maintenance and rehabilitation road works standards for each road class
Road Work Standards
Code | Standard
A | Very high
B | High
C | Medium
D | Low
E | Very low
F | Do minimum
G | Do nothing
Defined in RONET at: Capital Road Works Standards Configuration

## Slide 39: Asphalt Mix Roads Standards

## Slide 40: Optimal Standard
Least Total Society Costs
RONET determines optimal standard per road class

## Slide 41: Budget Scenarios
Optimal + 2 | Two standards above optimal standard per road class
Optimal + 1 | One standard above optimal standard per road class
Optimal | Optimal standard per road class
Optimal – 1 | One standard below optimal standard per road class
Optimal – 2 | Two standards below optimal standard per road class
Optimal – 3 | Three standards below optimal standard per road class
Do Minimum | Do minimum on all road classes
Do Nothing | Do nothing on all road classes
Custom | User defined standard per network type and traffic category

## Slide 42: An Example of Consequences to the Road Agency

## Slide 43: Consequences to Road Users

## Slide 44: Consequences to Society

## Slide 45: Consequences to Road Network Condition: Roughness (IRI in m/km)

## Slide 46: Road Works Details (M$)
Other Tables for: ($/km-year) ($/veh-km) (km/year) per surface class and surface type

## Slide 47: Road User Charges

## Slide 48: Next steps
Review RONET’s User Guide
RONET familiarization interactive exercise
Obtain as realistic as possible information on a road network of each participating country
Develop an optimum road network M&R program for the selected network
Prepare a brief report and present the results

## Slide 49: Cesar Queiroz SSATP/World Bank Consultant Former World Bank Highways Adviser Tel +1 301 755 7591 queiroz.cesar@gmail.com Washington, DC, USA

## Slide 50: RONET Team Exercise Road Network Two-lane Equivalent: Length, condition and traffic levels
This example of calculation is for primary roads. Please follow the example and obtain the lengths per cell for secondary and tertiary roads.

## Slide 51: Cesar Queiroz, former World Bank Highways Adviser, is an international consultant on roads and transport infrastructure. His main expertise is in public-private partnerships, road management and development, performance-based contracts, port reform and rehabilitation, improving governance, quality assurance and evaluation, research, teaching and training. Between 1986 and 2006, he held several positions with the World Bank, including Lead Highway Engineer and Principal Highway Engineer. Prior to joining the World Bank, Cesar was the deputy director of the Brazilian Road Research Institute in Rio de Janeiro. He holds a Ph.D. in civil engineering from the University of Texas at Austin, a M.Sc. in production engineering from the Federal University of Rio de Janeiro, and a B.Sc. in civil engineering from the Federal University of Juiz de Fora, Brazil. Cesar has published two books and more than 130 papers and articles. His recent assignments include infrastructure advisory services to Russia, Brazil, Latvia, Lithuania, Poland, Ukraine, Philippines, Uganda, Sri Lanka, India, Egypt, Colombia, Laos, Mozambique, Saudi Arabia, Tunisia, Sweden and Norway. He is currently a visiting professor at the University of Belgrade, Serbia, and has lectured on PPP at George Washington University since 1996, and at the International Law Institute since 2007.